## Slide 1
SUSTAINABILITY ROUNDTABLE, INC.
How the ERCOT Settlement Forecast Works
A plain-language guide for executive stakeholders
June 2026 · ERCOT Customer Portals · Confidential

## Slide 2
OVERVIEW
What the Forecast Is — and Isn't
Setting the context before the methodology
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
Purpose
The Projected Bill tab gives offtakers a rolling estimate of the current month's and next month's net settlement under their VPPA or CfD contract — before ERCOT publishes final settlement data (which lags ~60 days).
What it IS
• Weather-driven generation model calibrated to the plant's real metered output
• Forward price assumption entered by the user (or defaulted to trailing capture)
• Transparent: every assumption is visible and overridable
• Updated automatically each time the page loads
What it is NOT
• Final or invoiced settlement — that appears on the Past Settlement page
• A price forecast — the user supplies the forward price assumption
• A guarantee of future generation — weather and curtailment can differ
• An audited figure — for billing disputes, use the ERCOT data on the Invoice Audit page
• Retroactively binding — the model is refreshed on each visit; past estimates are not stored

## Slide 3
ARCHITECTURE
End-to-End: From Weather to Dollar
Five steps, three data sources, one settlement number
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
STEP 1
Weather Forecast
Open-Meteo API 16-day hi-res +35-day GEFS +ERA5 clim.
→
STEP 2
Height Extrap.
Wind speed scaled to hub height (Hellmann 1/7)
→
STEP 3
Generation Model
Solar: GHI÷1000 × capacity MW Wind: cubic power curve
→
STEP 4
Calibration Factor
Model ÷ SCED over last 60 days Anchors to real output
→
STEP 5
Settlement Calc.
Daily MWh × (market price − strike) = net $
Output: daily net settlement bar chart + month total, refreshed on every page load.

## Slide 4
DATA SOURCES
Three-Tier Weather Architecture
High-res near-term → ensemble mid-range → climatological tail
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
Days 1–16
Tier 1 — Standard Forecast
• Source: Open-Meteo (free, no API key)
• Model: ECMWF / GFS high-resolution NWP
• Solar: hourly GHI (W/m²), temperature
• Wind: hourly speed at 80 m and 120 m
• Updated: every page load (2-hr file cache)
• Also fetches 31 past days for context
Days 17–35
Tier 2 — GEFS Ensemble P50
• Source: Open-Meteo Ensemble API
• Model: GFS05 — 31 members averaged
• Ensemble mean = P50 (expected value)
• Wind: 80 m extrapolated to 120 m
• Updated: every 6 hours (4×/day)
• Boundary artifact trimmed automatically
Days 36–Month End
Tier 3 — Prior-Year ERA5
• Source: Open-Meteo Archive API (ERA5)
• Same calendar days from prior year
• Realistic day-to-day weather variation
• Better than a flat monthly average
• Cached 24 hrs (historical, stable)
• Flat historical shape used as backstop
Source priority: settled SCED actuals > Tier 1 > Tier 2 > Tier 3 > flat historical shape

## Slide 5
PHYSICS MODELS
How Weather Becomes MWh
Separate models for solar PV and wind — both anchored by a calibration factor
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
☀ Solar PV Model
Formula
MW = Capacity × (GHI W/m² ÷ 1,000) × Cal. Factor
Input
Hourly shortwave (GHI) from weather API
Capacity
Contracted MW share of the plant nameplate
Cal. Factor
Absorbs: panel efficiency (~17–20%), DC/AC losses, soiling, row shading, availability derating
Typical range
Cal. Factor ≈ 0.15–0.25 for a real PV plant (model is intentionally raw; factor corrects it)
Cap
Output capped at contracted capacity MW
🌬 Wind Model
Step 1
Extrapolate wind speed from 80/120 m to turbine hub height (Hellmann α = 1/7)
Step 2
Apply turbine power curve: < cut-in → 0 MW cut-in → rated → cubic ramp > rated → full capacity > cut-out → 0 MW (storm protection)
Turbine params
Per asset: Vestas V110 cut-out 20 m/s; Nordex N149 cut-out 25 m/s
Cal. Factor
Scales model to real SCED output; typically 0.5–1.5 for wind

## Slide 6
CALIBRATION
Anchoring the Model to Real Plant Output
The calibration factor is the single most important input
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
What is the Calibration Factor?
• A scalar multiplier applied to model output so the long-run average matches the plant's real SCED metering
• Computed as: Actual MWh ÷ Model MWh over the most recent 60 days of settled SCED data
• Absorbs all systematic differences between the simple weather model and the real plant (efficiency, losses, availability, curtailment, measurement error)
• Clipped to [0.05, 3.0] — values outside this range indicate a data problem, not a real plant behaviour
Data Source for Calibration
• Uses ERA5 archive (not the live forecast) for weather — live forecast zeros out radiation beyond ~30 days, but SCED lags ~60 days, so archive is essential
• SCED data sourced from ERCOT 15-min generation tables and scaled to the offtaker's contracted volume share
Example Cal. Factors (Live)
• Markum Solar: 1.231 (from 61 SCED days) → model produces 82% of actual output; factor corrects upward by 23%
• Azure Sky Wind: 1.108 (from 60+ SCED days) → model slightly understates output; factor adds ~11%
• Hidalgo Wind: derived from available SCED history
Consistency Guarantee
• The calibration step and the forecast step always use the same power curve parameters (cut-in, rated speed, cut-out) — ensuring the factor is meaningful and not distorted by a model mismatch

## Slide 7
SETTLEMENT MATH
From MWh to Dollars
VPPA / CfD settlement logic applied daily
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
Daily Net Settlement ($) = MWh × (Market Price − Strike Price)
Sign convention: positive = offtaker receives; negative = offtaker pays
MWh
• Forecasted daily generation at the contracted volume share
• Source priority: 1. Settled SCED (actuals) 2. Weather model × cal. factor 3. GEFS ensemble 4. ERA5 climatology
• Capped at contracted capacity MW
Market Price
• Real-time settlement point price ($/MWh) at the contract node
• For past settled days: actual ERCOT 15-min RT prices
• For forecast days: user-entered forward price assumption (defaults to trailing capture price from history)
• Not a modelled price — always a user assumption
Strike Price
• Fixed contract price in $/MWh (set in Contract Terms page)
• Markum Solar: $35.00/MWh
• Azure Sky Wind: $17.34/MWh
• Hidalgo Wind: $35.00/MWh
• When market > strike: offtaker RECEIVES the spread
• When market < strike: offtaker PAYS the spread

## Slide 8
KEY DRIVERS
What Moves the Forecast
Ranked by typical impact on the monthly net settlement
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
1
Forward Price Assumption
Largest single driver. The user sets this on the sidebar. A $5/MWh change on a 40,000 MWh month shifts the estimate by ±$200,000. Default is the trailing capture price from history.
High
2
Generation Forecast
Weather uncertainty compounds over the month. Near-term (16 days) is high-res and reliable. GEFS ensemble is P50 and less certain. ERA5 climatology adds typical-year variation.
Medium–High
3
Calibration Factor
Anchors the model to real output. Estimated from 60 days of SCED. Stable once enough history is available; unreliable on new plants with < 30 days of settled data.
Medium
4
Market Price Variability
Actual ERCOT prices are highly volatile (weather, demand, outages). The forward assumption smooths this. Large deviation events (e.g. winter storms) are not captured.
Low (estimate)
← Impact

## Slide 9
METHODOLOGY NOTES
Limitations & Transparency
What the model cannot do — and where to find the authoritative figures
Sustainability Roundtable, Inc. · Confidential
sr-inc.com
Known Limitations
• Weather beyond 35 days uses prior-year climatology — actual weather can differ significantly
• The power curve is a simplified cubic model; real turbine curves have smoother transitions
• No curtailment model — forecasted output may exceed what ERCOT actually dispatches
• Forward price is user-supplied — the tool does not forecast ERCOT market prices
• Calibration requires ~30+ days of settled SCED data; results on new plants are less reliable
• Extreme weather events (storms, heat waves) are not captured in the ensemble P50
Authoritative Data Sources
• Past Settlement (actual): ERCOT 15-min metered generation × real-time settlement prices
• Invoice Audit page: full interval-level detail, downloadable for billing verification
• Cross-check: EIA Form 923 monthly generation shown alongside SCED for independent validation
Free & Cited Data Sources
• Weather: Open-Meteo (open source, no API key) open-meteo.com
• Reanalysis: ERA5 via Open-Meteo Archive API (ECMWF reanalysis v5, hourly, global)
• Ensemble: GFS05 via Open-Meteo Ensemble API (NOAA GFS, 31-member, 35-day horizon)
• Generation: ERCOT SCED / MIS public data (15-min, plant-level, ~60-day lag)

## Slide 10
SUSTAINABILITY ROUNDTABLE, INC.
Key Takeaways
The forecast uses real weather data updated daily — not a static model
The calibration factor is the critical link between the weather model and real plant output
Near-term (16 days) is reliable; beyond 35 days is climatological context
The forward price assumption drives the dollar outcome — always user-controlled
Authoritative settlement figures are on the Past Settlement page, not the forecast
Questions? Contact Sustainability Roundtable, Inc. · sr-inc.com